## Slide 1: Network Design Elements & Network Threats
Dr. William Hutton, CISSP Washington State University

## Slide 2: Network Design
Considerations:
  Strategic Defense
  Tactical Defense
  Topology
    Physical v. Logical
    Segmentation
  Redundancy
  Resilience
Hardware:
  Hub
  Switch
  Router
Security:
  Firewalls
  IDS/IPS
  VPN
  Content filters

## Slide 3: Private IPv4 Ranges (IANA)
Class | Assigned Range
Class A | 10.0.0.0 – 10.255.255.255
Class B | 172.160.0.0 – 172.31.255.255
Class C | 192.168.0.0 – 192.168.255.255

## Slide 4: Types of Addresses
Unicast: Assigned to one interface of one host.
Anycast: Assigned to group of interfaces on multiple nodes. Packets are delivered to “first” interface only.
Multicast: Address assigned to group of interfaces on multiple nodes. Packets are delivered to all interfaces.
Broadcast: Unassigned. Packets are delivered to all hosts on the network.

## Slide 5: Types of Networks
Network | Description
LAN | Local area network
WAN | Wide area network (2+ LANS, typically one is an ISP.)
Internet | THE network of networks.
DMZ | DeMilitarized Zone (Internet (typically public) access to servers and information)
Intranet | Single company network that spans the Internet. (Typically involves VPN.)
Extranet | Multiple company networks that span the Internet. (Typicall involves multiple VPNs and DMZ.)
Cloud | Typically, SaaS, IaaS and Paas ([x]-as-a-Service)

## Slide 6: Intranet v. Extranet
Company Lambda
Company Alpha
Company Alpha ”Offsite”
DMZ
DMZ
Extranet
Intranet

## Slide 7: Network Segmentation (Traffic Isolation)
Subnetting (often physical)
  Increase security by compartmentalizing the network.
  More efficient use of IP address space (right-size number of hosts).
  Reduce broadcast traffic and “collisions” (less of a problem with more switches and less hubs).
VPN (often virtual) (Virtual Private Networking)
  Segment network
  Reduce collisions
  Boost performance
  Increase security
Notes: Devices that participate in a VLAN can be physically anywhere on the LAN.

## Slide 8: Network Ports (Inbound, Outbound, & Common Ports)
Port Range | Category | Description
0-1,023 | Well-Known (reserved) Ports | Commonly used protocols. Assigned by IANA. (e.g., HTTPS/443)
1,024-49,151 | Registered Ports | Vendor and proprietary applications. (e.g., RDP/3,389)
49,152 – 65,535 | Dynamic (ephemeral) and Private Ports | Unregistered. Often selected as “source ports” by OS.

## Slide 9: How Well-Known are these Well-Known Ports?
Port Number | Port Number
7 | 119
21 | 135
22 | 137-139
23 | 143
25 | 161
53 | 389
58 | 443
80 | 445
88 | 1433
110 | 3389
Notes: How many do you know? All are security concerns, but which especially dangerous?

## Slide 10: How Well-Known are these Well-Known Ports?
Port Number | Port Number
7 = Echo* | 123 = NTP
21 = FTP* | 135 = RPC**
22 = SSH | 137-139 = NetBIOS
23 = Telnet* | 143 = IMAP
25 = SMTP | 161 = SNMP*
53 = DNS* | 389 = LDAP*
58 = DHCP* | 443 = HTTPS
80 = HTTP | 445 = SMB*
88 = Kerberos* | 1433 = ODBC*
110 = POP | 3389 = RDP*
Notes: * Of particular security concern due to information leakage, plaintext protocol (i.e. unencrypted), authentication, configuration, remote access, or bypass

## Slide 11: Different Network Attacks
DoS
  DDoS
SYN Flood
Smurf (spoofed broadcast ICMP)
Fraggle (UDP Smurf)
Ping of Death (no longer works, but good example)
Fork Bomb
Spoofing
Session Hijacking
Man-in-the-Middle
DNS Poisoning
ARP Poisoning
MAC Flooding
VLAN Hopping
Null Session (e.g., C$)
Unauthorized Zone Transfers (i.e. DNS)
Reflection attacks
Exfiltration (e.g. Night Dragon)
Hardware (e.g., Spectre, Meltdown, Rowhammer, and BlackSmith)
Side-channel
Squatting
Ransomware