## Slide 1: Wireless Introduction
Ch. 1 (Beard 2016)

## Slide 2: Learning objectives
Describe how wireless communications have developed.
Explain the purpose of various generations of cellular technology.
Describe the ways mobile devices have revolutionized and will continue to revolutionize society.
Identify and describe future trends.

## Slide 3: Describe how wireless communications have developed.

## Slide 4
Notes: British inventors Cooke and Wheatstone patent the telegraph in 1837.

## Slide 5: Telegraph wires along Railroad Right-of-Way
Telegraph wires co-located with railway right-of-ways.
Telegraph stations co-located with railway stations .
First telegraph message (“What hath God wrought?” by Samuel Morse) sent in 1844.
  How were telegrams encoded?
  Was this encoding efficient?
”Hello world” example
Notes: Encoding: Morse
Efficiency: How would you determine this? (Symbol encoding—what’s involved?) [Work this out on paper/white board)
Carrier is altered (high / low voltage, digitally 1 or 0) = 2 states
Symbols: How many? 26 letters, 52 (upper/lower case), 62 (digits), more (punctuation). [ASCII = fixed-width, Morse=variable-width—optimized by not perfect (Huffman)].
Claude Shannon 100 years later would develop “A Mathematical Theory of Communication” then re-published as “THE Mathematical Theory of Communication”.

## Slide 6: What could Possibly go wrong?
R = L I
Notes: Ask students to brainstorm “cyber security” issues of telegraphs.
Responses should include confidentiality, integrity, availability attacks (Red threat). Facilitate brainstorming if necessary.
Carrington Event in 1859 (Solar cycle 10) geomagnetic storm caused fires along telegraph wires and stations. (Grey threat)
Risk = Likelihood x Impact (risk equation), but how do you measure impact? (ALE, etc.)

## Slide 7: Wireless comes of age
In 1896 Guglielmo Marconi invented the wireless telegraph, encoding alphanumeric symbols in an analog signal.
Five years later, he would transmit a wireless signal across the Atlantic ocean (~3,200 km).
20 years after that, amateur radio enthusiasts would accomplish their own transatlantic transmission (ARRL).
Led to the invention of radio, television, satellites, mobile telephones, mobile data.
More recently, wireless technology, cellular technology, mobile applications, Internet of Things.

## Slide 8
Notes: Wireless technology “shrinks the world” by simplifying the deployment of communication infrastructure (no wires) and allowing ideas to reach more people in more ways.
Ask for or give examples of different technologies.
Notice frequency increase (Y-axis) means more data over time (X-axis)

## Slide 9
Notes: 2007 documentary about the first satellite. You could hear it on 20 MHz if you had a short-wave radio.
https://www.military.com/history/russias-dead-hand-soviet-built-nuclear-doomsday-device.html

## Slide 10: The Global Cellular Network
~11M cell phone users in 1990
~7B in 2016
Convenient—move with people
Location aware by design
Gen. 1: AMPS (American Mobile Phone System)
Gen. 2: GSM (Global System for Mobile Communications
Gen. 3: CDMA2000 & UMTS (also wideband CDMA)
Gen. 4: WiMAX (IEEE 802.16) & LTE (Long Term Evolution)
5G Today
Notes: Contrast convenience w/ wired telephones that connected homes, not people.
Will cover ubiquitous aspects of previous generations; data, signal, transmission, etc.

## Slide 11: Mobile Device Revolution
Initial rush to wireless was voice only.
Innovations:
  Multi-Mb data access
  Longer battery life
  Smaller size
  >> MPx cameras
  Lower cost
Long distance 3G/4G and now 5G cellular
Wi-Fi IEEE 802.11 LANs
BlueTooth PANs

## Slide 12: Future Trends
Internet of Things (MTM or M2M communications)
  Discovery
  Trust
  Collaboration
Network densification (many small transmitters)
  Femtocells (indoors)
  Picocells (outdoors)
Device-centric architectures (”purpose-built networks”)
Massive MIMO (multiple inputs / multiple outputs to reach different locations)
mmWave (30 GHz to 300 GHz)
Notes: Expected 100-fold increase in devices.
Many short communications (take a look at your own PAN/LAN w/ WireShark—make an effort to create a “hyper-quiet” network)
MIMO allows a stationary wireless device to use different antennas and frequencies to transmit an optimal signal to different locations.
mmWave much higher frequencies (more bandwidth) but requires more power and has more attenuation—some limitations resolved by MIMO.

## Slide 13: The Trouble with Wireless
Transmission through objects
Reflections off objects
Signal scattering
Diffraction around edges of objects
Multiple copies of a signal arrive at the receiver at different times with attenuations, creating the problem of multipath fading.
Notes: Wireless does not always require a free line of site (90s “red balloon” antenna height calculations), depending on the frequency (Reception of distant AM radio stations at night.)

## Slide 14: Mitigation techniques
Modulation: Sends digital data in a signal format that sends as many bits as possible for the current wireless channel.
Error-control coding: Add extra bits to the signal so errors can be detected and corrected (FEC)
Adaptive modulation and coding: Dynamically adjust transmission based on current channel conditions.

## Slide 15: Mitigation techniques
Equalization: Counteracts multipath effects of a channel.
MIMO: Multiple antennas to point signals strongly in certain directions, send simultaneous signals in multiple directions or send parallel streams of data.
DSSS (Direct Sequence Spread Spectrum): Expands a signal over a wide bandwidth so problems in parts of the bandwidth are overcome.
OFDM (Orthogonal Frequency Division Multiplexing): Breaks a signal into many lower rate bit streams where each is less susceptible to multipath problems.

## Slide 16: Mitigation techniques
Modulation: Sends digital data in a signal format that sends as many bits as possible for the current wireless channel.
Error-control coding: Add extra bits to the signal so errors can be detected and corrected (FEC)
Adaptive modulation and coding: Dynamically adjust transmission based on current channel conditions.